## Slide 1: Vacuum-Assisted Wound Closure
(VAC)
Supervised by dr. Emad Aburajouh

## Slide 2: 01 02 03 04 05 WHO NEED TO USE IT WITH CONTRA-INDICATION HOW IT IS WORK ADVANTAGE DEFINTIONS TABLE OF CONTENTS
06
COMPLICATION

## Slide 3: WHAT IS THE WOUND ? 01.
It is any break in the skin or other body tissues caused by injury or surgical incision .

## Slide 4: SO… what is the VAC dressing ?
Is a method of decreasing air pressure around a wound to assist the healing. It’s also referred to as negative pressure wound therapy.

## Slide 5: HOW DOES IT WORK? 02.

## Slide 6: PARTS OF THE KIT ;
1 - polyurethane foam
2 - 2 x drapes (5 x drapes in the extra large)
3 - 1 x SensaT.R.A.C. Pad.
4 - Ruler

## Slide 7: PARTS OF THE Machine ;
1 - VACCUM PUMP removes air pressure over the wound.
2 - TUBE leads from under the adhesive film and connects to a portable vacuum pump
3 – DRESSING is put directly on the wound
4- adhesive film covers and seals the dressing and wound.

## Slide 8: Biological respone :
1-Remove of exudate and infectious material wich reduction of edema
2-promote perfusion and formation of granulation tissue

## Slide 9: Physical respone
1- wound edge are drawn together
2-cell surface strain (micro defromation tissue )

## Slide 10: less changing of wound dressings compared with other treatments increased blood flow to the wound decreased overall discomfort decreased swelling and inflammation decreased risk of bacterial infection gentle pulling together of the wound’s edges Wound VAC benefits

## Slide 11: APPLICATION
VIDEO

## Slide 12
Change (24-72h)

## Slide 13: APPLICATION
Safety margin = 2 INCH

## Slide 14: Who needs to use a wound VAC? 03.

## Slide 15: 1- Cesarean delivery (C-section)
VAC may help prevent infections after giving birth via cesarean delivery (more commonly known as a C-section).
A review of studiesTrusted Source found that VAC seemed to be able to decrease the number of infections and complications. (5-7 DAY)

## Slide 16: 2- BURNS
A retrospective reviewTrusted Source looked at the effectiveness of VAC for children with burn wounds or soft-tissue trauma.
The researchers found a link between third-degree burn wound size and the number of VACs received. They concluded VAC could be a safe and effective option that doesn’t cause excessive discomfort in children.

## Slide 17: 3- Traumatic and surgical wounds
VAC might be useful in the healing of traumatic injuries and postoperative wounds.
One review concluded that VAC has the potential to reduce infections after surgery. It also found that VAC may be more cost effective than traditional treatment options when hospital costs are taken into account.

## Slide 18: 4- Pressure ulcers
Pressure ulcers are sore skin spots caused by continuous pressure. VAC may be a suitable treatment option in some cases.
One studyTrusted Source looked at the use of VAC to heal a patient’s ulcer. Using VAC healed the ulcer in 6 weeks at half the cost of reconstructive surgery.

## Slide 19: Types of wounds not suitable for VAC ? 04.
VAC is suitable for a wide range of wounds. However, some types of wounds aren’t suitable for VAC. These include:

## Slide 20
cancer tissue
infected wounds
wounds near joints that may reopen with limb movement
fragile skin
areas with poor blood flow
exposed organs or blood vessels

## Slide 21: enteric fistula macerated skin, COMPLICATION bleeding bacterial infections
VERY RARE

## Slide 22: Dizziness OR nausea OR vomiting rash around your wound Headache OR diarrhea fever higher than (39°C ) bleeding around the wound Confusion OR sore throat WHEN TO STOP USING IT

## Slide 23: NOTES :
The length of time the procedure takes varies widely on the size and location of your wound.
VAC bandages should be changed two to three times a week. If your wound gets infected, the bandages may need changing more often.
Usually, a healthcare provider will change your bandages. In some cases, a family member or a caregiver can be trained to change your dressing.

## Slide 24: THANKS!