## Slide 1: Foley's catheter

## Slide 2
A foley's catheter is a flexable tube that is passed through the urethra and into bladder.
Foley catheter (named for Frederic Foley, who produced the original design in 1929)
The tube has two separated lumen. One lumen is open at both ends,and allows urine to drain out into a collection bag.
The other lumen has a valve on the outside end and connects to a ballon at the tip . The balloon is inflated with sterile saline when it lies inside the bladder, in order to stop it from slipping out.
Foly catheters are commonly made from sillicone rubber or natural rubber.

## Slide 3
  The size of a Foley's catheter is described using French unit(F). The most common size are 10F to 28F. F=0.33mm

## Slide 4: When Foley's catheters are used
-On patients who are anesthesized or sedated for surgery or in management of immobilized patients( e.g. pelvic fracture).
- On some urine incontinent patients.
- On patients whose prostate is enlarged to the point that urine flow from the bladder is cut off. The catheter is kept in until the problem is resolved.
-On patients with acute urinary retention with or without bladder outlet obstruction
-On patients with kidney disease and critically ill patiants whose urine output must be constantly and accurately measured hourly.

## Slide 5: Risks
-A major problem with Foley's catheter is that they have a tendancy to contribute to urinary tract infections(UTI) Approximately, 80% of health care-associated UTIs are related to the use of indwelling urinary catheters. This occurs because bacteria can travel up from catheter to bladder where the urine can become infected.
-If the balloon is opened before the Foley’s catheter is completely inserted in to the bladder .bleeding ; damage and even rupture of the urethra can occur.
-In some individuals, long_term permanent scarring and strictures of the urethra could occur.

## Slide 6: The procedure

## Slide 7: The doctor or medical assistant will insert the foly catheter in this manner:
the urethra and the surrounding areas are cleaned with a cotton ball dipped in antiseptic solution. Beginning at the urethra,the cleansing is performed in a circular motion,moving outward to the surrounding areas.
.a Foley catheter,lubricated with water soluble jelly,is inserted into the bladder through the urethra. .once the catheter is passed,the balloon is in the bladder. It is then slowly inflated with about 10cc of water using a syringe. Inflating the balloon should not be painful. .at this time,urine if present in the bladder should flow back through the catheter and into the sterile drainage bag.

## Slide 8: Drainage bag
while at the hospital the urinary drainage bag will be hung to the bedside rail by a hook on the bag ..if you need to be discharged from the hospital and sent home wearing the Foley catheter the drainage bag will be replaced with a portable drainage bag (leg bag).Adhesive tape will be used to hold the bag to the calf area. .removal of the catheter and bag .

## Slide 9
The catheter balloon is deflated by inserting a syringe into the catheter valve and pulling back on the syringe. .the pressure in the balloon will cause the water to flow into the syringe.once the balloon is empty the Foley catheter can be pulled out.

## Slide 10: Thank you
t