## Slide 1: Assessment Of Hearing
presented by:
Farah asaad al-ali
Hajer k. bani-doumi

## Slide 2: Physiology Of Hearing

## Slide 3: Physiology Of Hearing
Sound waves, collected by the Pinna, are transmitted along the Ear Canal to the Ear Drum, then it set the Ossicles into vibration. These Ossicles will amplify the vibration and transmit it from the Ear Drum to the Oval Window in the Inner Ear.
Here, The vibration triggers movement of the fluid in the Cochlea and sets the hair cells into vibration. When Hair Cells vibrate, they translate the incoming sound signals into electrical impulses, and send it to the Cochlear Nerve.
Nerve impulses are transmitted along the Vestibulocochlear Nerve to the Brain. In Central Auditory System, the impulse signals processes and translates into auditory information, so we can “hear”.

## Slide 4: Types Of Hearing Loss

## Slide 5: Clinical Assessment Of Hearing
Whispered Voice Test
Tuning Fork Tests
- Rinne’s Test
- Weber’s Test
Audiometry
- Pure Tone Audiometer
- Speech audiometer
- Impedance Audiometer
- Electric response audiometer

## Slide 6: Whispered Voice Test
Formal Assessment. Ask the patient to repeat words spoken by the examiner at different intensities & distances.
Examination sequence
  Stand behind the patient.
  Start with your mouth about 15 cm from the ear you are testing.
  Mask hearing in the other ear by rubbing the tragus.
  Ask the patient to repeat your words. Use a combination of multisyllable numbers and words (1,2,3 or A,B,C). Start with a normal speaking voice to confirm that the patient understands the test. Lower your voice intensity to a clear whisper.
  Repeat, but this time at arm's length from the patient's ear. People with normal hearing can repeat words whispered at 60 cm.

## Slide 7: Interpretation of Results…
Normal
Patient is able to hear whispered speech accurately.
Volume is the same in both ears.
Abnormal
The patient is unable to hear whispered speech.
The patient hears speech at a higher volume in one ear.
The patient hears sounds but does not understand words.

## Slide 8: Translating into numbers
Speech Level Required | Equivalent Hearing Loss
Quiet Whisper | Normal
Loud Whisper | 20-40 dB
Quiet Voice | 30-45 dB
Loud Voice | 45-60 dB
Shout | 60-80 dB

## Slide 9: Tuning Fork Tests
Two tuning fork tests are used to differentiate between conductive and sensorineural deafness using either a 512 Hz or a 256 Hz tuning fork.
- Rinne’s Test
- Weber’s Test

## Slide 11: Rinne’s Test
Compares the level of air and bone conduction of the same ear.
Examination Sequence
Place the vibrating prongs at the patient's external auditory meatus; ask if he can hear it.
Now place the still-vibrating base on the mastoid process. Ask: 'Is it louder in front, or behind your ear?'
Alternatively:
The Rinne’s test is performed by placing a vibrating tuning fork (512 or 256 Hz) initially on the mastoid process until sound is no longer heard, the fork is then immediately placed just outside the ear.
  Normally, the sound is audible at the ear.

## Slide 12: Rinne’s Test

## Slide 13: Interpretation of Results…
Normal Findings
Air conduction (AC) is better than bone conduction (BC) (AC > BC) this is Positive Rinne’s.
Abnormal Findings
Bone conduction is better than air (AC < BC) this is Negative Rinne’s and indicates conductive hearing loss.
In sensorineural deafness, bone conduction and air conduction are both equally depreciated, maintaining the relative difference of bone and air conductions.
  AC>BC but both are depressed.

## Slide 14: Additional Note
If hearing in one ear is extremely poor there may be a false negative Rinne’s.
  The sound will be conducted through the bone to the opposite ear and give a false impression of better BC.

## Slide 15: Weber’s Test
Examination Sequence:
  Place the base of the vibrating tuning fork in the middle of the patient's forehead.
  Ask: 'Where do you hear the sound?'
  Record which side Weber's test lateralizes to if not central.
Finding | Interpretation
No Lateralization (The sound is heard equally in both ears) | Normal/Healthy Patient
 | Bilateral symmetrical Conductive Deafness
 | Bilateral symmetrical Sensorineural Deafness
Lateralized to better/healthy ear | Unilateral Sensorineural Deafness
Lateralized to worse/affected ear | Unilateral Conductive Deafness

## Slide 16: Pure Tone Audiometry
Electronic device that generates tones for determining hearing thresholds. Displayed on a graphic plot called audiogram.

## Slide 17: Audiogram
Is a chart of hearing sensitivity ,with frequency charted on the (x-axis) and intensity on the (y-axis).

## Slide 18: Equipments
The necessary equipment depends on the testing method used and may include the following:
Headphones
Insert earphones
Speakers
Bone-conduction
oscillator

## Slide 19: Important Terms
Frequency is cycles per unit of time. Frequency is measured in hertz (Hz), which are cycles per second.
The ears are most sensitive to frequencies in the range of 1000-4000Hz.
The range of human speech is between 400-3000 Hz.
Usually frequencies of 250-8000 Hz are used in testing because this range represents most of the speech spectrum, although the human ear can detect frequencies from 20-20,000 Hz.
The hearing threshold is the sound level below which a person’s ear is unable to detect any sound. For adults, 0 dB is the reference level.

## Slide 20: Ranges of Hearing Loss
-10 – 20 dB HL = Normal range
21 – 40 dB HL = Mild hearing loss
41 – 55 dB HL = Moderate
56 – 70 dB HL = Moderately Severe
71 – 90 dB HL= Severe
Greater than 90 dB HL = Profound

## Slide 21: Audiogram Interpretation
hearing sensitivity by AC
hearing sensitivity by BC
AC/BC difference (a.k.a. the air-bone gap)
No air-bone gap = normal or SNHL
AC worse than BC = conductive hearing loss

## Slide 22: Normal Hearing

## Slide 23: Conductive Hearing Loss

## Slide 24: Conductive Hearing Loss
Conductive hearing loss has normal bone-conduction thresholds, but air-conduction thresholds are poorer than normal by at least 10 dB.
Conductive hearing loss is secondary to an outer ear or middle ear abnormality, which can include abnormalities of the tympanic membrane.
Examples of abnormalities include:
  Occlusion of the external auditory canal by cerumen or a mass
  Middle ear infection and/or fluid
  Perforation of the tympanic membrane
  Ossicular abnormalities

## Slide 25: Sensorineural Hearing Loss

## Slide 26: Sensorineural Hearing Loss
Sensorineural hearing loss has bone- and air-conduction thresholds within 10 dB of each other, and thresholds are higher than 25 dB HL.
Sensorineural hearing loss is secondary to cochlear abnormalities and/or an abnormality of the auditory nerve or central auditory pathways.
Examples include:
  Presbycusis
  Noise-induced hearing loss
  Ménière disease
  Retrocochlear lesions such as vestibular schwannoma

## Slide 27: Mixed Hearing Loss

## Slide 28: Mixed Hearing Loss
Mixed hearing loss has conductive and sensorineural components.
  Pure-tone air-conduction thresholds are poorer than bone-conduction thresholds by more than 10 dB.
  Bone-conduction thresholds are higher than 25 dB.

## Slide 29: Examples of Characteristic Audiograms

## Slide 30: Noise-induced Hearing Loss
Exposure to high-intensity noise may cause temporary or permanent hearing loss.
  Repeated exposure to noise trauma may change a temporary threshold shift (TTS) to a permanent threshold shift (PTS).
  However PTS can occur secondary to a single noise exposure in some cases.
  Degree of hearing loss depends on time exposure, sound intensity, and sound frequency characteristics.
Noise-induced hearing loss is typically greatest in the 4000- to 6000-Hz region.
Noise-induced hearing loss is sensorineural except in certain blast injuries with possible tympanic membrane and middle ear damage.

## Slide 31: Noise-induced Hearing Loss

## Slide 32: Otosclerosis
The condition is caused by stapedial fixation in the oval window, stiffening the middle ear system.
Otosclerosis causes a slowly progressive conductive or mixed hearing loss.
  Stapes fixation produces an audiometric artifact known as the Carhart notch, (Carhart notch :Isolated depression(20-30 Db) around 2000 Hz
  in the bone-conduction audiogram of patients with otosclerosis. )
Onset usually occurs when patients are aged 15-45 years, and otosclerosis is more common in women than in men.
  One half of patients report a family history of otosclerosis.

## Slide 33: Otosclerosis

## Slide 34: Ménière disease
It is idiopathic disease ,but it is believed to be linked to endolymphatic hydrops, an excess of fluid in the inner ear. It is thought that endolymphatic fluid bursts from its normal channels in the ear and flows into other areas, causing damage ( in the vestibular membrane).
Ménière disease affects the cochlear and vestibular systems.
  Attacks lasting from 20 minutes to several hours generally
  include some combination of vertigo, hearing loss,
  sensation of aural fullness, and tinnitus.
  Tinnitus and hearing loss may persist between attacks.

## Slide 35
Hearing loss is usually unilateral, at least in the early stages, usually in lower frequencies and fluctuant, but it typically develops into a permanent sensorineural hearing loss.
  Many patients report increased sensitivity to loud noises (recruitment) in addition to the listed symptoms.
Onset for approximately one half of patients occurs when aged 40-60 years. The disease is rare in children.

## Slide 36: Ménière disease Audiogram
Notes: Mild rising sensorineural hearing loss. Typically, however, the lower frequencies are affected more severely. This is due to preferential sensitivity of the apex to the hydrops.

## Slide 37: Unilateral SNHL Evident (Meniere(

## Slide 38: Presbycusis (Age-related hearing loss(
Presbycusis usually manifests as a bilateral and symmetrical sensorineural hearing loss.
Usually, the higher frequencies are most severely affected.
Onset of presbycusis typically occurs in middle-aged or older patients.
  Hearing loss is secondary to degeneration of the cochlea, cranial nerve VIII, and/or the central auditory system.
  The condition is usually slowly progressive.

## Slide 39: Presbyacusis

## Slide 40: Presbyacusis

## Slide 41: Speech audiometry
in this test, the patient's ability to hear and understand speech is measured. Two parameters are studied:
(i)Speech reception threshold
threshold (ii)Speech awareness

## Slide 42: speech-recognition threshold (SRT)
The speech-recognition threshold (SRT) is sometimes referred to as the speech-reception threshold.
  The objective of this measure is to obtain the lowest level at which speech can be identified at least half the time.
An SRT better than pure tone average by more than l0 dB suggests a functional hearing loss.

## Slide 43: Speech-awareness threshold (SAT)
Speech-awareness threshold (SAT) is also known as speech-detection threshold (SDT).
  The objective of this measurement is to obtain the lowest level at which speech can be detected at least half the time.
  This test does not have patients repeat words; it requires patients to merely indicate when speech stimuli are present

## Slide 44
The SAT is especially useful for patients too young to understand or repeat words.
The SAT may also be used for patients who (1) speak another language or who (2) have impaired language function because of neurological insult.
For patients with normal hearing or somewhat flat hearing loss, this measure is usually 10-15 dB better than the speech-recognition threshold (SRT) that requires patients to repeat presented words.

## Slide 45: Impedance audiometry
(Tympanogram)
The primary purpose of impedance audiometry is to determine the status of the tympanic membrane and middle ear via tympanometry
Principle o f impedance audiometry. (A) Oscillator to produce a tone
of 220 Hz.
(B) Air pump to increase or decrease air pressure in the ear canal.
(C) Microphone to pick up and measure sound pressure level reflected from the tympanic
membrane.

## Slide 46
A type A response suggests normal middle ear function, but it occurs in some otosclerotic ears, particularly in early stages.
Peak is between +/- 100 daPa
Compliance from 0.3-1.5 ml
Notes: “tent” shape the air pressure behind the tempanic membrane the same as the outer air canal

## Slide 47
Type As (A shallow) suggests a stiffened (less compliant) middle ear system.
Peak is between +/- 100 daPa
Compliance is less than 0.3 ml
This type may suggest, otosclerosis and malleus fixation..

## Slide 48
Type Ad High compliance at or near ambient pressure.
Peak is between +/- 100 daPa
Compliance is more than 1.5 m
Seen in ossicular discontinuity or thin and lax tympanic membrane.

## Slide 49: Type B tympanogram
Type B A flat or dome-shaped graph. No change in compliance with pressure changes. Seen in middle ear fluid or thick tympanic membrane.

## Slide 50: Type B tympanogram
Type B is a flat trace with no observed compliance or idmittance peak. Type B tympanograms must be interpreted in conjunction with ear canal volume readings.
  Average ear canal volumes for children are 0.5-1.0 mL.
  Average adult volumes are 1.0-1.5 mL.
Type B (normal ear canal volume) usually suggests otitis media.
Type B (small ear canal volume) may suggest that the ear canal is occluded with wax/debris or that the immittance probe is pushed against the side of the ear canal.
Type B (large ear canal volume) suggests a perforation of the tympanic membrane. (because middle ear volume is added up to the volume of external ear canal)

## Slide 51
Type C suggests significant negative pressure in the middle ear system and may suggest developing or resolving otitis media.
  Additionally, this type indicates a malfunctioning eustachian tube.
Peak is below –100 daPa
Compliance from 0.3-1.5 ml

## Slide 53: Acoustic reflex
It is based on the fact that a loud sound, 70 - 100 dB above the threshold of hearing of a particular ear, causes bilateral contraction of the stapedial muscles which can be detected by tympanometry
A person who feigns total deafness and does not give any response on pure tone audiometry but shows a positive stapedial reflex is
a malingerer

## Slide 54
Alternative Name: Auditory Brainstem Response (ABR) Audiometry

## Slide 55
Auditory brainstem response (ABR) audiometry is a neurologic test of auditory brainstem function in response to auditory (click) stimuli.
  It is a test of the central pathways.
ABR audiometry refers to an evoked potential generated by a brief click or tone pip transmitted from an acoustic transducer in the form of an insert earphone or headphone.
  The elicited waveform response is measured by surface electrodes typically placed at the the scalp and ear lobes.
Auditory brainstem response (ABR) audiometry has a wide range of clinical applications, including screening for retrocochlear pathology, universal newborn hearing screening, and intraoperative monitoring.

## Slide 57
The ABR waveform is ….
A useful mnemonic to recall the site of origin of the evoked potentials is E.COLI.
  E = Eight Cranial Nerve [Wave I/II]
  C= Cochlear Nucleus [Wave III]
  O= Olive (Superior Olive) [Wave IV]
  L= Lateral Lemniscus [Wave V]
  I= Inferior Colliculus [Wave VI]

## Slide 58
When interpreting the ABR, we look at:
amplitude (the number of neurons firing),
latency (the speed of transmission),
interpeak latency (the time between peaks),
and interaural latency (the difference in wave V latency between ears)

## Slide 59
Auditory brainstem response (ABR) audiometry is considered an effective screening tool in the evaluation of suspected retrocochlear pathology such as an acoustic neuroma or vestibular schwannoma.
  However, an abnormal ABR finding suggestive of retrocochlear pathology indicates the need for MRI of the cerebellopontine angle.

## Slide 60: Newborn being tested using AABR

## Slide 61
ABRs may be used to detect auditory neuropathy or neural conduction disorders in newborns.
  Because ABRs are reflective of auditory nerve and brainstem function, these infants can have an abnormal ABR screening result even when peripheral hearing is normal.
Infants that do not pass the newborn hearing screenings do not necessarily have hearing problems.
  When hearing loss is suspected because of an abnormal ABR screening result, a follow-up diagnostic threshold ABR test is scheduled to determine frequency-specific hearing status.

## Slide 63
The primary purpose of otoacoustic emission (OAE) tests is to determine cochlear status, specifically hair cell function.
This information can be used to:
  Screen hearing (particularly in neonates, infants, or individuals with developmental disabilities)
  Partially estimate hearing sensitivity within a limited range
  Differentiate between the sensory and neural components of sensorineural hearing loss.
  Test for functional (feigned) hearing loss
Does not measure the central pathway

## Slide 64: Risk factors for hear loss
Family history of permanent childhood sensorineural hearing loss
In utero infection such as cytomegalovirus, rubella toxoplasmosis, or herpes
Craniofacial anomalies, including those with morphological abnormalities of the pinna and ear canal)
Postnatal infections associated with sensorineural hearing loss, including bacterial meningitis
Syndromes associated with progressive hearing loss such as neurofibromatosis, osteopetrosis, and Usher syndrome
Neurodegenerative disorders, such as Hunter syndrome, or sensory motor neuropathies, such as Charcot-Marie-Tooth syndrome
Head trauma
Recurrent or persistent otitis media with effusion lasting for at least 3 months

## Slide 65: THANK YOU